## Slide 1: ENGI 301 <ThermoBuddy> Proposal
<02/19/2024>
<Marc De Guzman>

## Slide 2: Background Information
What is being proposed?
  A low-cost device that displays temperature and humidity, specifically meant for NICUs in low-income settings
    It alerts nurses/clinicians when the NICU is at unsafe conditions by playing an alarm and flashing the screen
    The threshold thermometer and humidity can be customized by the user
    Alerts when battery is low
  https://www.hackster.io/flygonial/pocketbeagle-air-quality-data-module-ad8ce1
  https://www.hackster.io/romannovosad11/indoor-air-quality-monitoring-system-66d386
What improvements / additions over existing project
  Runs on battery-power (Specified by clients)
  Has a big screen that can be read from about 10 m away
  User-friendly interface

## Slide 3: System Block Diagram
Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)
Pocket Beagle
(P2_11)
DHT22 Sensor
https://cdn-learn.adafruit.com/downloads/pdf/dht-humidity-sensing-on-raspberry-pi-with-gdocs-logging.pdf
GND (P1_16)
3.3V (P1_14)
CLK (P1_8)
MISO (P1_10)
MOSI (P1_12)
GPIO5 (P1_6)
GPIO89 (P1_4)
GPIO87 (P1_2)
SPI Screen
Buzzer
(P1_16) (P2_1)

## Slide 4: Power Block Diagram
Create a Power Block Diagram
  Label voltages / currents of components
Pocket Beagle
5 V (P2_13)
Ground (P2_15)
DHT22 Sensor
(P1_1)
5 V
(from Battery)
Buzzer
(P1_16) Ground
5 V (P1_14)
Ground (P1_16)
SPI Screen

## Slide 5: Components / Budget
Component | ENGI301 to Buy? | Cost
Screen https://www.adafruit.com/product/2354?gad_source=1&gclid=CjwKCAiA8sauBhB3EiwAruTRJjduw0nYuage31ffuhRgEgCXdWIeSrdvOL85wqC47gLQ6SzxxXuK-hoCy0IQAvD_BwE | Yes | $34.95
Buzzer https://www.adafruit.com/product/1536 | Yes | $0.95
DHT22 Sensor https://www.adafruit.com/product/385 | Yes | $9.95