## Slide 1: ENGI 301 <ThermoBuddy> Proposal
<02/19/2024>
<Marc De Guzman>

## Slide 2: Background Information
What is being proposed?
  A low-cost device that displays temperature and humidity, specifically meant for NICUs in low-income settings
    It alerts nurses/clinicians when the NICU is at unsafe conditions by playing an alarm and flashing the screen
    The threshold thermometer and humidity can be customized by the user
    Alerts when battery is low
  https://www.hackster.io/flygonial/pocketbeagle-air-quality-data-module-ad8ce1
  https://www.hackster.io/romannovosad11/indoor-air-quality-monitoring-system-66d386
What improvements / additions over existing project
  Runs on battery-power (Specified by clients)
  Has a big screen that can be read from about 10 m away
  User-friendly interface

## Slide 3: System Block Diagram
Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)
Pocket Beagle
(P2_9)
(P2_11)
AHT10 Sensor
https://cdn-learn.adafruit.com/downloads/pdf/dht-humidity-sensing-on-raspberry-pi-with-gdocs-logging.pdf
(P2_9)
(P2_11)
(P2_23)
(P2_21)
7 segment displays
Buzzer
(P1_16) (P2_1)
(P1_1)
Battery and Battery Detector
May add LEDs to incorporate a blinking component to the device, but I want to focus more on putting the main functionality with the buzzer first.

## Slide 4: Power Block Diagram
Create a Power Block Diagram
  Label voltages / currents of components
Pocket Beagle
5 V (P2_13)
Ground (P2_15)
AHT10 Sensor
(P1_1)
5 V
(from Battery)
Buzzer
(P1_16) Ground
3.3 V (P2_23)
Ground (P2_21)
7 segment displays

## Slide 5: Components / Budget
Component | ENGI301 to Buy? | Cost
Red 7-segment Display (4 Digit) https://www.adafruit.com/product/1264 | Yes (Order 2 displays) | $15
Buzzers (3) https://www.adafruit.com/product/1536 | Yes | $2.85
AHT 10 Sensor https://www.amazon.com/HiLetgo-Precision-Temperature-Measurement-Communication/dp/B09KGVSKBY?source=ps-sl-shoppingads-lpcontext&ref_=fplfs&psc=1&smid=A30QSGOJR8LMXA | Yes | $7.99
Small 7 segment display (4 Digit) Link | Yes | $8.99
Battery Display https://www.adafruit.com/product/5383 | Yes | $2.95